ES500-MR-7710C4

Feature

| · | Camera CCD | Sony Color CCD or Sharp Color CCD Option |
| --- | --- | --- |
| · | Resolution | 700TVL(650/600/540/420) TVL option |
| · | Infrared LED | 24pcs Xφ5 Leds |
| · | IR Distance | 25-30M |
| · | Mini. Illumination | 0Lux(IR on) |
| · | Lens | 4mm(3.66/812mm option) |

| Model NO. | ES500-MR-7710C4 | ES500-MR-7510C4 |
| --- | --- | --- |
| VIDEO |
| Image Device | 1/3" Sony Color CCD | 1/3" Sony Super HAD CCD |
| Total Pixels | PAL:795(H)*596(V) ; NTSC:811(H)*508(V) | PAL:537(H)*597(V) ; NTSC:537(H)*505(V) |
| Effective Pixels | PAL:752(H)*582(V) ; NTSC:768(H)*494(V) | PAL:500(H)x582(V) ; NTSC:510(H)x492(V) |
| Effective Pixels | 2:1 Interlace |
| Scanning System | Internal |
| Synchronization | 700TVL | 600TVL |
| Min. Illumination | 0Lux(IR on) |
| S/N Ratio | More than 48dB |
| Video Output | 1Vp-p,75ohm, BNC |
| LENS |
| Lens | 4mm(3.6/6/8/12mm option) |
| OPERATIONAL |
| Day & Night | Auto |
| BLC | Auto |
| Gain Control | Auto |
| White Balance | Auto |
| E-Shutter | PAL:1/50 ~ 1/100,000sec; NTSC:1/60 ~ 1/100,000sec |
| Infrared LED | 24pcs Xφ5 |
| IR Distance | 25-30 Meters |
| ENVIRONMENTAL |
| Operation Temperature | -10°C ~ +50°C |
| Storage Temperature | -20°C ~ +60°C |
| Vandal-proof Casing | YES |
| ELECTRICAL |
| Input Voltage/ Current | DC12V 300mA |
| Adapter Requirement | DC12V1A |
| MECHANICAL |
| Color | White |
| Dimensions | 98*75mm |